## Slide 1: COE 372 Sem2, 2022/23
Digital Systems Design Methodologies

## Slide 2: Lecture Overview
VLSI
VLSI Design
Design Abstraction Levels
Design Tools
Design Methodologies
Complexity and Design
Design Hierarchy and Modularity
Summary

## Slide 3: VLSI: Very Large Scale Integration
Integration: Integrated Circuits
  multiple devices on one substrate
How large is Very Large?
  SSI (small scale integration)
    7400 series
  MSI (medium scale)
    74000 series
  LSI
  VLSI
  ULSI/SLSI/GSI

## Slide 4: VLSI Design
The real issue with VLSI is about designing systems on chips (SOCs).
SOC designs are complex
To manage complexity of design, one needs
  to use structured design techniques, and
  sophisticated design tools
Another fact is that technology becomes out of date sooner
  So develop and use techniques that will transcend today’s technology

## Slide 5: The Process of VLSI Design
Consists of many different representations/Abstractions of the system (chip) that is being designed
  System Level Design
  Architecture / Algorithm Level Design
  Digital System Level Design
  Logical Level Design
  Electrical Level Design
  Layout Level Design
  Semiconductor Level Design (possibly more)
Each abstraction/view is itself a Design Hierarchy of refinements which decompose the design

## Slide 6: Design Abstraction Levels

## Slide 7: Computer Aided Design tools
Tools
  Editors
  Simulators
  Libraries
  Module Synthesis
  Place/Route
  Chip Assemblers
  Silicon Compilers
Experts
  Logic design
  Electronic/circuit design
  Device physics
  Artwork
  Applications – system design
  Architectures

## Slide 8: VLSI Design Methodologies
Methodologies which are based on:
  System Level Abstractions vs. Device Characteristic Abstractions
    Logic structures and circuitry change slowly over time
      trade-offs do change, but the choices do not
  Scalable Designs
    Layout techniques also change slowly
      But the minimum feature size steadily decreases with time (also Voltage, Die Size, etc.)

## Slide 9: VLSI Design Flow (1)
(Y-chart representation)

## Slide 10: The Y-chart Representation (1)
The Y-chart consists of three major domains
  Behavioral domain,
  Structural domain,
  Geometrical layout domain.

## Slide 11: The Y-chart Representation (2)
The design flow starts from the algorithm that describes the behavior of the target chip. The corresponding architecture of the processor is first defined.
It is mapped onto the chip surface by floorplanning. The next design evolution in the behavioral domain defines finite state machines (FSMs) which are structurally implemented with functional modules such as registers and arithmetic logic units (ALUs).
These modules are then geometrically placed onto the chip surface using CAD tools for automatic module placement followed by routing, with a goal of minimizing the interconnects area and signal delays. The third evolution starts with a behavioral module description.

## Slide 12: The Y-chart Representation (3)
Individual modules are then implemented with leaf cells. At this stage the chip is described in terms of logic gates (leaf cells), which can be placed and interconnected by using a cell placement & routing program.
The last evolution involves a detailed Boolean description of leaf cells followed by a transistor level implementation of leaf cells and mask generation. In standard-cell based design, leaf cells are already pre-designed and stored in a library for logic design use.

## Slide 13: VLSI Design Flow (2)

## Slide 14: VLSI Design Flow (3)
The design flow is divided in the two parts:
Front End Design:
  Front-end design includes most of the steps in the flow prior to physical design. (system specification and functional design)
Back End Design:
  Starting with physical design and beyond is considered the back-end of the design flow.

## Slide 15: Design hierarchy & modularity

## Slide 16: Complexity and Design
Creating a design team for a VLSI project
  Needing hundreds of engineers, scientists, and technicians
  Needing hierarchy design and many different “Level Views”
  Everyone of each level depends upon the Computer-Aided Design (CAD) tools
  Each member gets the opportunity to study small sections of the system

## Slide 17: Design Hierarchy (1)
System specifications: is defined in both general and specific terms, such as functions, speed, size, etc.
Abstract high-level model: contains information on the behavior of each block and the interaction among the blocks in the system
Logic synthesis: To provide the logic design of the network by specifying the primitive gates and units needed to build each unit

## Slide 18: Design Hierarchy (2)
Circuit design: where transistors are used as switches and Boolean variables are treated as having signal values varying between two levels of voltage
Physical design: the network is built on a tiny area on a slice of silicon
Manufacturing: a completed design process is moved on to the manufacturing line

## Slide 19: Design Hierarchy (3)
Hierarchical design
  Top-down design
    The initial work is quite abstract and theoretical and there is no direct connection to silicon until many steps have been completed
    Acceptable in modern digital system design
    Co-design strategy of combining HW/SW is critical
    Similar to Cell-based Design Flow
  Bottom-up design
    starts at the silicon or circuit level and builds primitive units such as logic gates, adders, and registers as the first steps
    Acceptable for small projects
    Similar to Full-custom Design Flow

## Slide 20: Design Hierarchy (4)

## Slide 21: Design Hierarchy (Example) (1)

## Slide 22: Design Hierarchy (Example) (2)
Based on “divide and conquer”
Dividing a module into sub- modules and then repeating this operation on the sub-modules until the complexity of the smaller parts becomes manageable.
On previous slide, CMOS four-bit adder is split into its components.
The adder can be decomposed progressively into one-bit adders, separate carry and sum circuits, and finally, into individual logic gates. At this lower level of the hierarchy, the design of a simple circuit realizing a well-defined Boolean function is much easier to handle than at the higher levels of the hierarchy.

## Slide 23: ASIC Types
At the engineering level, Application Specific ICs are classified by the approach used to implement and build the circuit
  Full-custom Design: where every circuit is custom designed for the project
    Extremely tedious
    Time-consuming process
  Semi-custom Design: to reduce design workload and time
    Use a group of primitive predefined cells as building blocks (cells) from a cell library

## Slide 24: Modularity and other Concepts
The hierarchical design approach reduces the design complexity by dividing the large system into several sub-modules. Usually, other design concepts and design approaches are also needed to simplify the process.
  Regularity
  Locality

## Slide 25: Modularity
Modularity in design means that the various functional blocks which make up the larger system must have well-defined functions and interfaces.
Modularity allows that each block or module can be designed relatively independently from each other.
All of the blocks can be combined with ease at the end of the design process, to form the large system.
The concept of modularity enables the parallelisation of the design process.

## Slide 26: Regularity
Decomposition of a large system in simple and similar blocks as much as possible.
Example:
  Design of array structures consisting of identical cells—such as a parallel multiplication array.

## Slide 27: Locality
The concept of locality also ensures that connections are mostly between neighbouring modules, avoiding long-distance connections as much as possible.

## Slide 28: Summary (1)
VLSI
  How large is integration?
VLSI Design
  Flow and process
Design Abstraction Levels
  System
  Module
  Gate
  Circuit
  Device
Design Tools

## Slide 29: Summary (2)
Design Methodologies
  System level and Device characteristics Abstractions
  Scalable designs
  Y-chart
Complexity and Design
  Design project team
Design Hierarchy and Modularity
  Modularity
  Regularity
  Locality